## Slide 1: Hot Work Program
OSHA regulations dictate that CSP has a hot work program.
This program is used to determine what procedures are needed while preforming hot work
This program is designed so that the work is done safely in accordance with OSHA regulations.

## Slide 2: Hot Work Program
Hot work is defined by OSHA as, any work that can provide an ignition source for combustibles such as:
  Oil rags
  Gas cylinders
  Gas cans
  Paper

## Slide 3: Hot Work Program
Hot work permit is issued when performing work that could cause a fire such as:
  Welding
  Burning
  Brazing
  Propane Soldering
  Oxyacetylene Cutting
  Grinding Metals

## Slide 4: Components of a Hot Work Program
A Hot Work Program typically includes the following:
  A document of procedure
  Hot work permit use and application
  Trained employees and contractors involved
  Ongoing review and monitoring of the program

## Slide 5: Written Procedure
A written procedure should be developed by the shift lead or the control room operator to:
  Establish the goal
  Designate roles and responsibilities
  Steps taken so hot work can be performed safely
  Review the procedure and train everyone involved
  Make sure permit is filled out correctly and filed once work is complete

## Slide 6: Hot Work Permit
The Permit lists all the requirements:
  Remove all combustibles materials away 35ft or more. If danger can’t be removed, use a fire blanket to cover .
  Atmospheric analysis result if necessary
  Fire alarms, and fire extinguishers locations
  If a fire watch is necessary
  Wind direction if necessary
  Flammables in trenches near by
  All workers be trained in for the hot work permit

## Slide 7: Atmospheric Test
Work must be discontinued:
  If the alarm sounds.
  If the LEL (lower explosive limit) is greater than 50
  If oxygen is less than 19.5%
  If oxygen is greater than 23.5%

## Slide 8: Fire Watch
When to post a fire watch:
  When combustibles located within 35ft can’t be removed
  When wall or flooring combustibles are within 35ft radius
  When it is deemed necessary by the shift lead or control room operator

## Slide 9: Fire Watch Responsibilities
The responsibilities of a fire watch are as follows:
  Have appropriate fire extinguisher ready
  Monitor the site at all times and 30mins after work is complete
  Sound alarm if there is a fire
  Fight the fire only to the capacity of the equipment being used
  Remove any tape when work is done
  Notify the control room or supervisor that work is complete.

## Slide 10: Fire Watch
While the fire watch designee has designated duties, it is up to everyone, including contractors and operators, to ensure all hot work is done in a safe manner.

## Slide 11: Control Room/ Facility Manager
Once work is finished the control room/ manager of the facility should take appropriate actions:
  Complete work is done and so is permit
  Shall also file permit for records and further review