## Slide 1
Respiratory Protection Program

## Slide 2: OSHA Requirements
In the control of occupational diseases caused by breathing air contaminated with harmful dusts, fogs, fumes, mists, gases, smokes, sprays, or vapors, the primary objective shall be to prevent atmospheric contamination.
This shall be accomplished as far as feasible by accepted engineering control measures

## Slide 3: OSHA Requirements
Examples of engineering control measures are:
  Enclosure or confinement of the operation,
  General and local ventilation,
  Substitution of less toxic materials.
When effective engineering controls are not feasible, or while they are being instituted, appropriate respirators shall be used.

## Slide 4: OSHA Requirements
The employer shall:
  Provided a respirator to each employee when such equipment is necessary to protect the health of such employee.
  Provide the respirators which are applicable and suitable for the purpose intended.
  Be responsible for establishing and maintaining a respiratory protection program
    Make sure the respirator is used in compliance with the conditions of its certification.

## Slide 5: OSHA Requirements
The employer shall:
  Make sure the program covers each employee required by the work conditions to use a respirator.
  Select and provide the respirator based on the hazards that affect the employee and the user factors that affect the respirator performance:
    A reasonable estimate of employee exposures to respiratory hazard(s)
    Identification of the contaminant's chemical state and physical form.

## Slide 6: OSHA Requirements
The employer shall
  Consider the atmosphere to be Immediately Dangerous to Life or Health ( IDLH ) whenever the employer cannot reasonably estimate the employee exposure.
  Select NIOSH certified respirator from a sufficient number of models and sizes so that it is acceptable to, and correctly fits, the user.
  Develop and implement a written respiratory protection program with required worksite-specific procedures and elements for respirator use.
  Administer the program via a suitably trained program administrator.

## Slide 7: Program Procedures
The program must include:
  Provisions to update the program as necessary to reflect changes in workplace conditions that affect respirator use.
  Procedures for selecting respirators for use in the workplace
  Medical evaluations of employees required to use respirators
  Fit testing procedures for tight-fitting respirators;
  Procedures for proper use of respirators in routine and reasonably foreseeable emergency situations;

## Slide 8: Program Procedures
The program must include:
  Procedures and schedules for cleaning, disinfecting, storing, inspecting, repairing, discarding, and maintaining respirators
  Training of employees in the proper use of respirators, putting on and removing them, limitations on their use, and their maintenance
  Procedures for regularly evaluating the effectiveness of the program.

## Slide 9: Medical Evaluation Procedures
The employer shall
  Provide a medical evaluation to determine the employee's ability to use a respirator, before the employee is fit tested or required to use the respirator in the workplace.
  Identify a physician or other licensed health care professional (PLHCP) to perform medical evaluations using a medical questionnaire or an initial medical examination
  Obtain a written recommendation regarding the employee's ability to use the respirator from the PLHCP.

## Slide 10: Medical Evaluation Procedures
The recommendation shall provide only the following information:
  Any limitations on respirator use related to the medical condition of the employee, or relating to the workplace conditions in which the respirator will be used, including whether or not the employee is medically able to use the respirator
  The need, if any, for follow-up medical evaluations;
  A statement that the PLHCP has provided the employee with a copy of the PLHCP's written recommendation.

## Slide 11: Fit Test
Before an employee may be required to use any respirator with a negative or positive pressure tight-fitting facepiece, the employee must be fit tested with the same make, model, style, and size of respirator that will be used.
The employer shall:
  Ensure that employees using a tight-fitting facepiece respirator pass an appropriate qualitative fit test (QLFT) or quantitative fit test (QNFT)

## Slide 12: Fit Test
The employer shall
  Ensure that an employee using a tight-fitting facepiece respirator is fit tested prior to initial use of the respirator, whenever a different respirator facepiece (size, style, model or make) is used, and at least annually thereafter.
  Conduct an additional fit test whenever the employee reports, or the employer, PLHCP, supervisor, or program administrator makes visual observations of, changes in the employee's physical condition that could affect respirator fit.

## Slide 13: Additional Fit Test
Such conditions include, but are not limited to, facial scarring, dental changes, cosmetic surgery, or an obvious change in body weight.
If after passing a QLFT or QNFT, the employee subsequently notifies the employer, program administrator, supervisor, or PLHCP that the fit of the respirator is unacceptable, the employee shall be given a reasonable opportunity to select a different respirator face piece and to be retested.

## Slide 14: Respirator use
CSP has adopted a standard procedure where respirator cartridges must be changed every 12 months, on expiration date, on fit-test, or after each use.
Loading Hydrochloric Acid
  Respirators are worn during the connect and disconnect process as a precaution
  The use of full face respirators is required
When not in use, the half-face respirator is stored in the personal locker in the changing-rooms
Escape respirators are intended for visitors use

## Slide 15: Respirator use
Respirators must not be used when concentration of gases is unknown
Respirators must not be used when facial hair is present that could interfere with the seal
Respirators must not be modified
Respirators must be cleaned with a damp cloth and sanitizing wipe after each use.
Never use hot water above 110 F to clean a respirator
Cartridges must be changed at least every six months

## Slide 16: Respirator use
Employees must follow a 5 step procedure when ever there is need to maintain a respirator, or after each use
  Headbands: Check to see they have their elasticity. Look for cracks or tears.
  Face Piece: Check for dirt, cracks, tears, or holes. Inspect for distortion and make sure rubber is still flexible.
  Inhalation/Exhalation Valves: Check for cracks, tears, dirt, and build up of materials.
  Cartridge Holders: Check gaskets and look for possible damage to threads.
  Cartridge/Filters: Make sure they are clean and undamaged. Do NOT clean using compressed air.

## Slide 17: Respirator use
Follow this procedure when donning the respirator:
  See that straps lie flat on head
  Tighten lower “neck” straps
  Tighten the “side” straps
  Place both hands on headband pad and push it towards the neck
  Tighten “neck” and “side” straps again
  Tighten forehead or “front” strap a few notches if necessary
  Always perform a seal check by placing a palm over the exhale valve and gently exhale. Then place hands over the cartridges/filters and gently inhale till mask collapses

## Slide 18: Definitions
Hazardous Atmospheres: Atmosphere that contains contaminant (s) in excess of the allowable limit or has less than 19.5% oxygen.
Immediately Dangerous to Life and Health (IDLH): Atmosphere that poses an immediate threat to life, or would impair an individual’s ability to escape.

## Slide 19: Definitions
Protection Factor: A ratio of the air contaminate concentration outside the respirator to the air contaminate inside the respirator
  A protection factor of 10 means that the respirator can reduce air contaminates by a factor of 10
Maximum Use Concentration: The mathematical product of the permissible exposure limit (PEL) and the assigned protection factor
  Chlorine has a PEL of 0.5ppm. If you have a respirator with a protection factor of 10, then the maximum use concentration would be 5ppm (0.5ppm x 10 = 5ppm)

## Slide 20: Definitions
User Seal Check: An action performed by the user to ensure a proper seal each time the mask is worn
IDHL for chlorine is defined at 10 ppm in air
NIOSH: National Institute for Occupational Safety and Health.
  NIOSH is the official research body of OSHA. Results of research and investigation are used to make recommendations to OSHA