## Slide 1
Management of Change

## Slide 2: Management of Change
This presentation explains methods by which changes to the facility, process or utility, other than "like for like" substitution, will be properly evaluated for their impact on quality, safety, health, loss prevention and the environment prior to implementation and that such changes and evaluations will be properly documented.

## Slide 3: Management of Change Types
Replacements in Kind A "like for like" replacement (meets design specifications) of a system, a piece of equipment or a procedure with one identical to the one being replaced.
Process Change An alteration, whether temporary or permanent, that could affect the control or integrity of a process that goes beyond the established safe operating range, recipe or proven raw material supplier.

## Slide 4: Management of Change Process Changes
  Process Technology, such as:
    Raw materials,
    Process chemistry,
    Process controls or conditions,
    Process recipes,
    Order of addition,
    Equipment design or material of construction,
    Piping or equipment specifications,
    Process safety information.
  Procedures
    Simple edits of procedures that do not change the actual procedure itself can be done without requiring an MOC. i.e. a name change, changes in terminology, etc.

## Slide 5: Management of Change Process Changes
Operating Discipline, such as:
  Computer controls,
  Additions or deletions of alarms.
  Bypassing safety systems, interlocks or controls.
Modifications, such as:
  Addition or removal of process equipment,
  Addition or removal of piping,
  Operating conditions, e.g. impeller size,
  Packaging procedures.
Services, such as:
  Equipment,
  Warehouse.

## Slide 6: Management of Change Process Changes
A Process Change is NOT:
  A change of set points within the range prescribed in procedures,
  Replacement with "like for like" equipment,
  A change, during an emergency, that is made to allow the safe shutdown of the process or unit. This type of change needs to be documented in unit or process logbooks and returned to the pre-change status as soon as possible,
  Preventative or routine maintenance, if care is exercised to prevent inadvertent change,
  Personnel changes.

## Slide 7: Management of Change Requirements
  All changes to a process, facility or utility shall require proper documentation prior to implementing the proposed change.
  The proposed change might be as simple as increasing the inventory of a certain chemical or as severe as bypassing an equipment interlock due to an outage.
  Generally, any change will require the origination and approval of proper forms
  An entry in an “operations log book” does not qualify as proper documentation of change.
  Once approved, the forms will be routinely reviewed. Copies of the approved forms shall be maintained to facilitate these reviews.

## Slide 8: Management of Change Forms
Maintenance Work Order Form:
  A written work order system shall be used for all routine cases of repair, in kind replacement or similar actions.
  The work order shall include an inspection component to give the originator an opportunity to identify a true “change.”
  Proper documentation of this type of work is necessary to ensure that all employees can routinely identify when it does occur.
  The Work Order Form may be originated by any employee, and must be approved by the Facility Manager or his designate.
  The “Manager’s Section” may only be completed by the Facility Manager.

## Slide 9: Management of Change Procedure
Submitting a Management of Change Request
  A “Management of Change” form must be completed:
    When there is an obvious change proposed.
    When individuals are not confident that they have the knowledge or skills to render a proper decision.
    Any employee may originate this form, that must be approved by two managers.
    Authority to release a proposed change for implementation is prohibited until the Facility Manager confirms that approval has been achieved.
  All Work orders must be closed out in a timely fashion, and retained for auditing purposes.

## Slide 10: Management of Change Procedure
Conditions of Approval:
In certain circumstances supplementary conditions may be required for MOC approval. These conditions will be documented and returned with the approved MOC. All the delineated conditions must be met as a condition of approval
RESPONSIBILITIES
Any individual responsible for a function may assign or delegate performance of that function to other suitably qualified people. The individual originally assigned shall retain responsibility and accountability for proper execution of the delegated activity.

## Slide 11: Management of Change Procedure
The Facility Manager shall:
  Submit the MOC to the appropriate manager for approval.
  Provide training to enable employees to recognize change.
  Involve employees by providing the opportunity for their input in analyzing change for hazard analysis and process operability.
    CSP uses the following mechanisms to communicate and embrace changes:
      Work Orders
      Change notification
      Routinely Tuesday meetings
      Ad hoc meetings as needed

## Slide 12: Management of Change Procedure
The Facility Manager shall:
  Properly modify operating documents and instructions so as to comply with requirements of this procedure.
  Train all affected employees on the change, and their responsibilities resulting from the change.
  In the case of a temporary change, ensure the affected equipment/area is returned to its “pre-change” status
  Document and properly maintain necessary MOC files.